## Slide 1: Using R to Introduce Students to Principal Component Analysis, Cluster Analysis, and Multiple Linear Regression
David Harvey
Pittcon 2018
http://bit.ly/2j10Hai

## Slide 2
http://bit.ly/2j10Hai

## Slide 3
Context
http://bit.ly/2j10Hai

## Slide 4: Chem 351: Chemometrics
http://bit.ly/2j10Hai
Unit 1: Introduction
Unit 2: Basic Statistics
Unit 3: Distribution of Data
Unit 4: Confidence Intervals
Unit 5: Analysis of Variance
Unit 6: Linear Regression
Unit 7: 3D Visualizations
Unit 8: Experimental Design
Unit 9: Signal Processing
Unit 10: Principal Component Analysis
Unit 11: Cluster Analysis
Unit 12: Multiple Linear Regression
This course, Chem 351: Chemometrics, provides an introduction to how chemists and biochemists can extract useful information from the data they collect in lab, including, among other topics, how to summarize data, how to visualize data, how to test data, how to build quantitative models to explain data, how to design experiments, and how to separate a useful signal from noise.
Two 60 minute class periods per week for 14 weeks. Course is divided into 12 units.

## Slide 5: R as a Tool for Teaching Chemometrics
data-centric programming language and environment for statistical computing
large number of users ensures longevity of software
base installation provides access to a wide variety of computational methods for processing data and tools for visualizing data
highly extensible through user-written scripts and packages of functions
available via Free Software Foundation’s GNU General Public License
versions for UNIX, Linux, Windows, and MacOS platforms
easy to interweave text, tables, and figures
base packages are very stable so code is resilient
http://bit.ly/2j10Hai
for further details regarding R, see https://www.r-project.org/
Make R a tool, not a barrier. Emphasis is on adapting coding examples, using coding templates, using available packages, and using functions provided by instructor

## Slide 6: The Analytical System: Beer’s Law
stock standards
  0.0500 M Cu2+
  0.1000 M Co2+
  0.0375 M Cr3+
  0.1300 M Ni2+
  all in 0.10 M HNO3
samples prepared from stocks
  single metal ions
  binary mixtures of metal ions
  ternary mixtures of metal ions
  quaternary mixtures of metal ions
  Spectra collected with a Vernier SpectroVis Plus spectrometer using Logger Pro 3 for data acquisition. Individual spectra exported as separate.csv files, combined into a single file, cleaned up, and saved as a single .csv file.
  File has 80 rows (one per sample) and 642 columns (seven with information on composition of samples and absorbance values at 635 wavelengths).
  This data set is brought into R using the readr package’s read_csv( ) function and then further subsetted within R to create individual data files.
  R functions: readr::read_csv( )
http://bit.ly/2j10Hai

## Slide 7
Prelude
http://bit.ly/2j10Hai

## Slide 8: External Standardization for Copper
Al,Cu = el,CubCCu
plot spectra for set of standards and identify the wavelength of maximum absorbance
  R functions: matplot( ), legend( ), which.max( ), abline( )
l = 809.1 nm
http://bit.ly/2j10Hai

## Slide 9: External Standardization for Copper
Coefficients: Estimate Std. Error t value Pr(>|t|)
(Intercept) 0.003202 0.008222 0.389 0.723
cuStd_conc 12.778883 0.247900 51.548 1.61e-05 ***
---Signif. codes: 0 ‘***’ 0.001 ‘**’ 0.01 ‘*’ 0.05 ‘.’ 0.1 ‘ ’ 1
Residual standard error: 0.007839 on 3 degrees of freedom
Multiple R-squared: 0.9989, Adjusted R-squared: 0.9985
F-statistic: 2657 on 1 and 3 DF, p-value: 1.608e-05
Al,Cu = el,CubCCu
plot spectra for set of standards and identify the wavelength of maximum absorbance
plot calibration data and determine equation for calibration curve
A = 12.78 M–1 × C + 0.0032
  R functions: plot( ), lm( ), abline( ), summary( )
http://bit.ly/2j10Hai

## Slide 10: External Standardization for Copper
$Prediction[1] 0.02322567
$`Standard Error`[1] 0.0006847376
$Confidence[1] 0.002179141
$`Confidence Limits`[1] 0.02104653 0.02540481
Al,Cu = el,CubCCu
plot spectra for set of standards and identify the wavelength of maximum absorbance
plot calibration data and determine equation for calibration curve
determine concentration of copper in an unknown using the chemCal package
  R functions: chemCal::inverse.predict( ), arrows( )
Ccu = 0.0232 M ± 0.0022 M
http://bit.ly/2j10Hai

## Slide 11: Analysis of Binary Mixture: Cu and Ni
Al1,mix = el1,CubCCu + el1,NibCNi
Al2,mix = el2,CubCCu + el2,NibCNi
plot spectra for a Cu standard, for a Ni standard, and for a mixture, and identify the wavelengths to use for the analysis
l1 = 809.1 nm
l2 = 394.2 nm
  R functions: plot( ), lines( ), legend( ), which.max( ), abline( )
http://bit.ly/2j10Hai

## Slide 12: Analysis of Binary Mixture: Cu and Ni
e809.1,Cub = 12.78 M–1 and e394.2,Cub = 0.017 M–1
e809.1,Nib = 0.837 M–1 and e394.2,Nib = 4.870 M–1
Al1,mix = el1,CubCCu + el1,NibCNi
Al2,mix = el2,CubCCu + el2,NibCNi
plot spectra for a Cu standard, for a Ni standard, and for a mixture, and identify the wavelengths to use for the analysis
plot calibration data and determine values for eb for each metal at each wavelength
  R functions: plot( ), legend( ), lm( ), abline( )
http://bit.ly/2j10Hai

## Slide 13: Analysis of Binary Mixture: Cu and Ni
CCu = 0.0182 M and CNi = 0.0506 M
Al1,mix = el1,CubCCu + el1,NibCNi
Al2,mix = el2,CubCCu + el2,NibCNi
plot spectra for a Cu standard, for a Ni standard, and for a mixture, and identify the wavelengths to use for the analysis
plot calibration data and determine values for eb for each metal at each wavelength
use R’s solve function to calculate concentrations of copper and nickel in mixture
  R functions: matrix( ), colnames( ), rownames( ), solve( )
2×2 matrix of eb values
Cu Ni
809.1 nm 12.77888326 0.8369356
394.2 nm 0.01747073 4.8700205
2×1 matrix of absorbance values
mixture
809.1 nm 0.2789825
394.2 nm 0.2415476
calculate 2×1 matrix of concentrations where [eb] × [conc] = [abs]
mixture
Cu 0.01858748
Ni 0.04953220
http://bit.ly/2j10Hai

## Slide 14
Main Event
http://bit.ly/2j10Hai

## Slide 15: Matrix Notation for Beer’s Law (A = ebC)
one analyte: one sample with absorbance measured at one wavelength
[A]1 sample × 1 wavelength = [C]1 sample × 1 analyte × [eb]1 analyte × 1 wavelength
two analytes: two samples with absorbance measured at two wavelengths
[A]2 samples × 2 wavelengths = [C]2 samples × 2 analytes × [eb]2 analytes × 2 wavelengths
overdetermined system: more samples and wavelengths than analytes
[A]8 samples × 5 wavelengths = [C]8 samples × 2 analytes × [eb]2 analytes × 5 wavelengths + [RE] 8 samples × 5 wavelengths
generalize: n analytes, s samples, and w wavelengths where n ≤ smaller of s or w
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
http://bit.ly/2j10Hai

## Slide 16: How Does PCA Work?
Suppose we have 21 samples and that we measure two properties—first variable and second variable—for each sample giving a matrix of data, [D], that has 21 rows and 2 columns.
[D]21 x 2
  R functions: seq( ), rnorm( ), scale( ), plot( ), abline( )
http://bit.ly/2j10Hai

## Slide 17: How Does PCA Work?
Linear regression provides the line of best fit to the data and explains more of the data’s overall variance than either of the two individual variables; we call this the first principal component.
  R functions: lm( ), abline( )
http://bit.ly/2j10Hai

## Slide 18: How Does PCA Work?
each sample has a score
each variable has a loading
Projecting the data onto the regression line gives the location of the data on the first principal component; these are called scores, (S). The cosines of the angles between the first principal component and each of the original axes are called loadings, (L).
[D]21 x 2 = [S]21 x 1 × [L]1 x 2
  R functions: points( )
http://bit.ly/2j10Hai

## Slide 19: How Does PCA Work?
Projecting the original data onto a line that is perpendicular to the first principal component gives the second principal component and adds in a second set of scores and loadings.
[D]21 x 2 = [S]21 x 2 × [L]2 x 2
  R functions: abline( ), points( )
http://bit.ly/2j10Hai

## Slide 20: How Does PCA Work?
Projecting the original data onto a line that is perpendicular to the first principal component gives the second principal component and adds in a second set of scores and loadings.
[D]21 x 2 = [S]21 x 2 × [L]2 x 2
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
  R functions: abline( ), points( )
http://bit.ly/2j10Hai

## Slide 21: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
[1] 380.5 414.9 449.3 483.7 517.9 550.6 583.2 613.3
[9] 642.9 672.7 703.3 735.5 767.8 800.2 832.6 868.7
  R functions: plot( ), lines( ), abline( ), legend( ), as.numeric( ), colnames( )
http://bit.ly/2j10Hai

## Slide 22: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
PC1 PC2 PC3 PC4
Standard deviation 3.3134 2.1901 0.42561 0.17585
Proportion of Variance 0.6862 0.2998 0.01132 0.00193
Cumulative Proportion 0.6862 0.9859 0.99725 0.99919
  R functions: prcomp( ), plot( ), summary( )
http://bit.ly/2j10Hai

## Slide 23: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
examine and interpret scores for first two principal components
  R functions: plot( )
http://bit.ly/2j10Hai

## Slide 24: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
examine and interpret scores for first two principal components
  R functions: plot( ), factor( ), legend( )
http://bit.ly/2j10Hai

## Slide 25: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
examine and interpret scores for first two principal components
examine and interpret biplot of loadings and scores for the first two principal components
  R functions: biplot( )
http://bit.ly/2j10Hai

## Slide 26: PCA: Worked Example
http://bit.ly/2j10Hai

## Slide 27: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
examine and interpret scores for first two principal components
examine and interpret biplot of loadings and scores for the first two principal components
  R functions: plot( ), colorRampPalatte( ), as.numeric( ), cut( )
http://bit.ly/2j10Hai

## Slide 28: PCA: Worked Example
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
examine and interpret scores for first two principal components
examine and interpret biplot of loadings and scores for the first two principal components
  R functions: par( ), plot( ), scatterplot3d::scatterplot3d
http://bit.ly/2j10Hai

## Slide 29: How Does Cluster Analysis Work?
  R functions: plot( )
Suppose we have six samples and that we measure two properties—a and b—for each sample and create a scatterplot of the data.
http://bit.ly/2j10Hai

## Slide 30: How Does Cluster Analysis Work?
  R functions: plot( ), segments( ), points( )
Find the two points that are closest to each other; this is the first cluster. Find the midpoint between the two points and define it as the position of the first cluster.
http://bit.ly/2j10Hai

## Slide 31: How Does Cluster Analysis Work?
  R functions: plot( ), segments( ), points( )
Find the next two points that are closest to each other; this is the second cluster. Find the midpoint between the two points and define it as the position of the second cluster.
http://bit.ly/2j10Hai

## Slide 32: How Does Cluster Analysis Work?
  R functions: plot( ), segments( ), points( )
Continue until all of the original data points are included in a cluster.
http://bit.ly/2j10Hai

## Slide 33: How Does Cluster Analysis Work?
  R functions: dist( ), hclust( ), plot( )
Plot a dendrogram, which shows the connectivity between points and clusters of points in terms of the distance (heights) separating them.
http://bit.ly/2j10Hai

## Slide 34: Cluster Analysis: Worked Example
  R functions: dist( )
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
calculate the distance between the individual data points using one of the available methods
1 2 3 4 5
2 1.53328104
3 1.73128979 0.96493008
4 1.48359716 0.24997370 0.77766228
5 1.49208058 0.32863786 0.68852029 0.09664215
6 1.49457333 0.42903074 0.57495499 0.21089686 0.11755129
http://bit.ly/2j10Hai

## Slide 35: Cluster Analysis: Worked Example
  R functions: hclust( ), plot( )
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
calculate the distance between the individual data points using one of the available methods
identify clusters and calculate and plot the heights between them using one of the available methods
http://bit.ly/2j10Hai

## Slide 36: Cluster Analysis: Worked Example
  R functions: plot( ), rect.hclust( )
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
calculate the distance between the individual data points using one of the available methods
identify clusters and calculate and plot the heights between them using one of the available methods
interpret dendrogram
http://bit.ly/2j10Hai

## Slide 37: Cluster Analysis: Worked Example
  R functions: par( ), plot( ), rect.hclust( ), t( )
http://bit.ly/2j10Hai
Subset of data consisting of 24 of the 80 samples: stock Cu, stock Co, stock Cr, five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
calculate the distance between the individual data points using one of the available methods
identify clusters and calculate and plot the heights between them using one of the available methods
interpret dendrogram

## Slide 38: How Does MLR Work?
[A]s × w = [C]s × n × [eb]n × w
Suppose we measure the absorbance at W wavelengths for S individual standard solutions with known concentrations for each of the N analytes. We can use these to determine amatrix of eb values for each analyte at each wavelength.
[C]Tn × s × [A]s × w = [C]Tn × s × [C]s × n × [eb]n × w
([C]Tn × s × [C]s × n)–1 ×[C]Tn × c×[A]s × w = ([C]Tn × n×[C]s × n)–1 ×[C]Tn × s×[C]s × n×[eb]n × w
([C]Ts × n × [C]s × n)–1 ×[C]Ts × n×[A]s × w = [eb]n × w
http://bit.ly/2j10Hai

## Slide 39: How Does MLR Work?
[A]s × w = [C]s × n × [eb]n × w
Having found the eb matrix, we can use it to calculate the concentrations for each of the N analytes in S samples given the absorbance for each sample at each wavelength.
[A]s×w×[eb]Tw×n = [C]s×n×[eb]n×w×[eb]Tw×n
[A]s×w×[eb]Tw×n× ([eb]n×w×[eb]Tw×n)–1 = [C]s×n×[eb]n×w×[eb]Tw×n× ([eb]n×w×[eb]Tw×n)–1
[A]s×w×[eb]Tw×n× ([eb]n×w×[eb]Tw×n)–1 = [C]s×n
http://bit.ly/2j10Hai

## Slide 40: MLR: Worked Example
Standards are subset of data consisting of 15 of the 80 samples: five each prepared from stock Cu, stock Co, and stock Cr. Samples are subset of data consisting of 21 of the 80 samples: five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
use absorbance values for a set of standards to calculate the eb values
  R functions: findeb( )*
380.5 414.9 449.3 483.7 517.9 550.6 583.2 613.3
concCu 0.5484511 0.1086153 0.1340763 0.1556545 0.1947192 0.3612272 0.6875421 1.3197158
concCo 0.7117778 0.7918523 2.5371205 4.0549583 4.5779242 2.0489508 0.5975168 0.3914665
concCr 13.2668054 15.1576056 6.9958232 4.0685312 6.7662738 12.0692592 13.6134665 9.8289364
http://bit.ly/2j10Hai
  * script written for this purpose

## Slide 41: MLR: Worked Example
  R functions: findconc( )*
http://bit.ly/2j10Hai
Standards are subset of data consisting of 15 of the 80 samples: five each prepared from stock Cu, stock Co, and stock Cr. Samples are subset of data consisting of 21 of the 80 samples: five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
use absorbance values for a set of standards to calculate the eb values
use absorbance values for the samples and the calculated eb values to give the predicted concentrations of the analytes
concCu concCo concCr
[1,] -0.00024 0.05991 0.00696
[2,] -0.00037 0.04939 0.01050
[3,] 0.00036 0.03926 0.01488
[4,] 0.00075 0.03088 0.01879
[5,] -0.00031 0.01947 0.02227
[6,] 0.01040 0.06076 0.00079
predicted concentrations of analytes
  * script written for this purpose

## Slide 42: MLR: Worked Example
  R functions: as.matrix( ), data.frame( )
concCu concCo concCr
[1,] 0.000 0.06 0.00750
[2,] 0.000 0.05 0.01125
[3,] 0.000 0.04 0.01500
[4,] 0.000 0.03 0.01875
[5,] 0.000 0.02 0.02250
[6,] 0.010 0.06 0.00000
http://bit.ly/2j10Hai
Standards are subset of data consisting of 15 of the 80 samples: five each prepared from stock Cu, stock Co, and stock Cr. Samples are subset of data consisting of 21 of the 80 samples: five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
use absorbance values for a set of standards to calculate the eb values
use absorbance values for the samples and the calculated eb values to give the predicted concentrations of the analytes
compare predicted and actual concentrations
concCu concCo concCr
[1,] -0.00024 0.05991 0.00696
[2,] -0.00037 0.04939 0.01050
[3,] 0.00036 0.03926 0.01488
[4,] 0.00075 0.03088 0.01879
[5,] -0.00031 0.01947 0.02227
[6,] 0.01040 0.06076 0.00079
predicted concentrations of analytes
actual concentrations of analytes

## Slide 43: MLR: Worked Example
  R functions: as.matrix( ), data.frame( ), apply( ), which.max( ), abs( ), round( )
concCu concCo concCr
-0.000304 -0.000199 -0.000315
concCu concCo concCr
0.001102 0.000857 0.000662
concCu concCo concCr
±0.002298 ±0.001787 ±0.001381
Cu: 0.00219 (0.02719 vs. 0.0250)
Co: 0.00176 (0.05176 vs. 0.0500)
Cr: 0.00173 (0.00173 vs. 0)*
* exceeds 95% confidence interval
http://bit.ly/2j10Hai
Standards are subset of data consisting of 15 of the 80 samples: five each prepared from stock Cu, stock Co, and stock Cr. Samples are subset of data consisting of 21 of the 80 samples: five Cu/Co binary mixtures, five Cu/Cr binary mixtures, five Co/Cr binary mixtures, six Cu/Co/Cr ternary mixtures.
use absorbance values for a set of standards to calculate the eb values
use absorbance values for the samples and the calculated eb values to give the predicted concentrations of the analytes
compare predicted and actual concentrations
report mean errors, standard deviations for errors, confidence intervals for errors, and identify maximum error for each analyte

## Slide 44: Acknowledgments
students in Chem 351
Brian Saulnier
DePauw University’s Faculty Development Committee
stackoverflow
http://bit.ly/2j10Hai

## Slide 45
http://bit.ly/2j10Hai

## Slide 46: Preparation of Standards & Mixtures
stock standard solutions
  0.0500 M Cu2+ (row 1)
  0.1000 M Co2+ (row 6)
  0.0375 M Cr3+ (row 11)
  0.1300 M Ni2+ (row 16)
  all in 0.10 M HNO3
additional single metal standards
  rows 2-5, 7-10, 12-15, 17-20
  10, 20, 30, 40 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
binary mixtures
  rows 21-25, 38-47, 60-64, 71-80
  30:10, 25:15, 20:20, 15:25, 10:30 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
ternary mixtures
  rows 32-37, 48-59, 65-70
  15:5:25, 25:5:15, 5:15:25, 25:15:5, 5:25:15, 15:25:5 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
quarternary mixtures
  rows 26-31
  3:3:7:7, 3:7:3:7, 3:7:7:3, 7:3:3:7, 7:3:7:3, 7:7:3:3 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3

## Slide 47: Spectra for Copper Standards
allSpec = read.csv("allSpec.csv")
wavelengths = as.numeric(colnames(allSpec[8:642]))
matplot(wavelengths, t(allSpec[1:5, 8:642]), type = "l", lwd = 2, xlab = "wavelength (nm)", ylab = "absorbance)
legend("topleft", legend = c("0.0500 M", "0.0400 M", "0.0300 M", "0.0200 M", "0.0100 M"),
lty = 1:5, lwd =2, col = 1:5, bty = "n")
id = which.max(allSpec[1,8:642])
abline(v = wavelength[id], lwd = 2, lty = 2)

## Slide 48: Calibration Curve for Copper Standards
plot(x = allSpec[1:5, 4], y = allSpec[1:5, id+7], xlab = "concentration (M)", ylab = "absorbance", pch = 19, col = "blue", xlim = c(0, allSpec[1,4]), ylim = c(0, allSpec[1,id+7]))
cu.lm = lm(allSpec[1:5,id+7] ~ allSpec[1:5,4])
abline(cu.lm, lwd = 2, col = "blue", lty = 2)
grid( )
summary(cu.lm)
Coefficients: Estimate Std. Error t value Pr(>|t|)
(Intercept) 0.003202 0.008222 0.389 0.723
allSpec[1:5, 4] 12.778883 0.247900 51.548 1.61e-05 ***
---Signif. codes: 0 ‘***’ 0.001 ‘**’ 0.01 ‘*’ 0.05 ‘.’ 0.1 ‘ ’ 1
Residual standard error: 0.007839 on 3 degrees of freedom
Multiple R-squared: 0.9989, Adjusted R-squared: 0.9985
F-statistic: 2657 on 1 and 3 DF, p-value: 1.608e-05
A = 12.78 M–1 × C + 0.0032

## Slide 49: What is PCA? How Does it Work?
Suppose we have 21 samples and that we measure two properties for each sample giving a matrix of data that has 21 rows and 2 columns.
[data]21 x 2
Linear regression provides the line of best fit and explains more of the variance than either of the individual variables; we call this the first principal component.
Projecting the data onto the regression line gives the location of the data on the first principal component; these are called scores. The cosine of the angles between the first principal component and each of the original axes are called loadings.
[data]21 x 2 = [scores] 21 x 1 × [loadings] 1 x 2 + [re] 21 x 2
Projecting the original data onto a line perpindicular to pc1 gives pc 2 and
[data]21 x 2 = [scores] 21 x 2 × [loadings] 2 x 2 + [re] 21 x 2

## Slide 50: What is PCA? How Does it Work?
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w

## Slide 51: Preparation of Standards & Mixtures
stock standard solutions
  0.0500 M Cu2+
  0.1000 M Co2+
  0.0375 M Cr3+
  0.1300 M Ni2+
  all in 0.10 M HNO3
additional single metal standards
  10, 20, 30, 40 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
binary mixtures
  30:10, 25:15, 20:20, 15:25, 10:30 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
ternary mixtures
  15:5:25, 25:5:15, 5:15:25, 25:15:5, 5:25:15, 15:25:5 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
quaternary mixtures
  3:3:7:7, 3:7:3:7, 3:7:7:3, 7:3:3:7, 7:3:7:3, 7:7:3:3 mLs of stock solutions
  diluted to 50 mL with 0.10 M HNO3
  Spectra collected using a Vernier SpectroVis Plus spectrometer and Logger Pro 3 for data acquisition. Individual spectra exported as .csv files, combined, and cleaned up in Excel prior to reading into R. This data set was further subsetted within R to create individual data files.

## Slide 52: Structure of Master Data File
filename: allSpec.csv
dimensions: 80 rows by 642 columns
columns
  1: sample id
  2: analyte id
  3: dimension (no. analytes; 1, 2, 3, or 4)
  4: concentration of Cu
  5: concentration of Co
  6: concentration of Cr
  7: concentration of Ni
  8–642: wavelengths (635 values from 380.5 nm to 899.5 nm)
rows
  1–5: Cu solutions
  6–10: Co solutions
  11–15: Cr solutions
  16–20: Ni solutions
  21–25: Cr/Co mixtures
  26–31: Cr/Cu/Ni/Co mixtures
  32–37: Cr/Ni/Co mixtures
  38–42: Cu/Co mixtures
  43–47: Cu/Cr mixtures
  48–53: Cu/Cr/Co mixtures
  54–59: Cu/Cr/Ni mixtures
  60–64: Cu/Ni mixtures
  65–70: Cu/Ni/Co mixtures
  71–75: Ni/Co mixtures
  76–80: Ni/Cr mixtures

## Slide 53: PCA: Examining the Loadings
plot(ex_one.pca$rotation, type = "o")
text(x = ex_one.pca$rotation[,1]+0.02, y = ex_one.pca$rotation[,2]+0.02, labels = wavelengths[wavelength_ids - 7], cex = 0.75)

## Slide 54: Analysis of Binary Mixture: Cu and Ni
# create 2x2 matrix of eb values with rows defined by wavelengths and column by analytes
eb = matrix(data = c(eb_cu1 = cu.lm1$coefficients[2], eb_cu2 = cu.lm2$coefficients[2], eb_ni1 = ni.lm1$coefficients[2], eb_ni2 = ni.lm2$coefficients[2]), nrow = 2, ncol = 2, byrow = FALSE)
colnames(eb) = c("Cu", "Ni")
rownames(eb) = c("809.1 nm", "394.2 nm")
# create 2x1 matrix of absorbance values with rows defined by wavelengths and column by samples
abs = matrix(data = c(allSpec[62, cu.id], allSpec[62, ni.id]), nrow = 2, ncol = 1, byrow = FALSE)
colnames(abs) = "mixture”
rownames(abs) = c("809.1 nm", "394.2 nm")
# calculate 2x1 matrix of concentrations using the solve function where [eb] x [conc] = [abs]
solve(eb, abs)
CCu = 0.0182 M
CNi = 0.0506 M
# create 2x1 matrix of absorbance values with rows defined by wavelengths and column by samples
abs = matrix(data = c(mixture[idcu], mixture[idni]), nrow = 2, ncol = 1, byrow = FALSE)
colnames(abs) = "mixture”
rownames(abs) = c("809.1 nm", "394.2 nm")
abs
mixture
809.1 nm 0.2749761
394.2 nm 0.2465907
# calculate 2x1 matrix of concentrations using the solve function where [eb] x [conc] = [abs]
solve(eb, abs)
[,1]
Cu 0.01820605
Ni 0.05056911

## Slide 55: PCA for a Ternary Mixture
[A]s × w = [C]s × n × [eb]n × w + [RE] s × w
choose a subset of the original 635 wavelengths
perform PCA and determine relative importance of the 16 principal components
examine scores for first two principal components
examine biplot of loadings and scores for the first two principal components
  R functions: biplot( )

## Slide 56: Chem 351: Chemometrics
http://bit.ly/2j10Hai
Unit 1: Introduction
Unit 2: Basic Statistics
Unit 3: Distribution of Data
Unit 4: Confidence Intervals
Unit 5: Analysis of Variance
Unit 6: Linear Regression
Unit 7: 3D Visualizations
Unit 8: Experimental Design
Unit 9: Signal Processing
Unit 10: Principal Component Analysis
Unit 11: Cluster Analysis
Unit 12: Multiple Linear Regression
This course, Chem 351: Chemometrics, provides an introduction to how chemists and biochemists can extract useful information from the data they collect in lab, including, among other topics, how to summarize data, how to visualize data, how to test data, how to build quantitative models to explain data, how to design experiments, and how to separate a useful signal from noise.
Two 60 minute class periods per week for 14 weeks. Course is divided into 12 units.

## Slide 57: R as a Tool for Teaching Chemometrics
data-centric programming language and environment for statistical computing
large number of users ensures longevity of software
base installation provides access to a wide variety of computational methods for processing data and tools for visualizing data
highly extensible through user-written scripts and packages of functions
available via Free Software Foundation’s GNU General Public License
versions for UNIX, Linux, Windows, and MacOS platforms
easy to interweave text, tables, and figures
base packages are very stable so code is resilient
http://bit.ly/2j10Hai
for further details regarding R, see https://www.r-project.org/

## Slide 58
The Analytical Context
Qualitative and Quantitative Analysis
of Multicomponent Mixtures Using Beer’s Law

## Slide 59: Analysis of Binary Mixture: Cu and Ni
CCu = 0.0182 M and CNi = 0.0506 M
Al1,mix = el1,CubCCu + el1,NibCNi
Al2,mix = el2,CubCCu + el2,NibCNi
plot spectra for a Cu standard, for a Ni standard, and for a mixture, and identify the wavelengths to use for the analysis
plot calibration data and determine values for eb for each metal at each wavelength
use R’s solve function to calculate concentrations of copper and nickel in mixture
  R functions: matrix( ), colnames( ), rownames( ), solve( )
# create 2x2 matrix of eb values with rows defined by wavelengths and column by analytes
eb = matrix(data = c(eb_cu1 = cu.lm1$coefficients[2], eb_cu2 = cu.lm2$coefficients[2], eb_ni1 = ni.lm1$coefficients[2], eb_ni2 = ni.lm2$coefficients[2]), nrow = 2, ncol = 2, byrow = FALSE)
colnames(eb) = c("Cu", "Ni")
rownames(eb) = c("809.1 nm", "394.2 nm")
# create 2x1 matrix of absorbance values with rows defined by wavelengths and column by samples
abs = matrix(data = c(allSpec[62, cu.id], allSpec[62, ni.id]), nrow = 2, ncol = 1, byrow = FALSE)
colnames(abs) = "mixture"
rownames(abs) = c("809.1 nm", "394.2 nm")
# calculate 2x1 matrix of concentrations using the solve function where [eb] x [conc] = [abs]
solve(eb, abs)
http://bit.ly/2j10Hai